## Slide 1: 1) Structural Symmetry 2) Bookshelf Problem
Jake Blanchard
Fall 2009

## Slide 2: Making Use of Problem Symmetry
Reflective or mirror symmetry exists if there is symmetry of geometry, loads, and properties with respect to a plane.
Other symmetry types exist, but are less common
Another type – Axisymmetry uses special element formulations rather than boundary conditions and will be studied later in the course.
Anti-symmetry
P
Rotational Symmetry

## Slide 3: Using Symmetry
Using symmetry reduces problem size (also modeling time) and can simplify boundary conditions.
Symmetry b.c.
p
p
Symmetry b.c.
p
Symmetry b.c.
Or
Ux = 0
Rotz = 0

## Slide 4
E=200 GPa
=0.3
Thickness=3 mm
Plane Stress
Fillet radius is 2 cm
p=0.2 MPa
Find max Von Mises stress
10 cm
20 cm
2 cm

## Slide 5: To easily vary fillet radius…
File/Write db log file…
  Choose write essential commands only
Edit file and change radius
File/Clear and Start New
File/Read input from…

## Slide 6: My Log File Listing
/PREP7
!*
ET,1,PLANE82
!*
KEYOPT,1,3,3
KEYOPT,1,5,0
KEYOPT,1,6,0
!*
!*
R,1,.003,
!*
!*
MPTEMP,,,,,,,,
MPTEMP,1,0
MPDATA,EX,1,,200e9
MPDATA,PRXY,1,,0.3
BLC4,0,0,.2,.02
BLC4,.2,0,-.02,-.08
FLST,2,2,5,ORDE,2
FITEM,2,1
FITEM,2,-2
AADD,P51X
!*
LFILLT,9,8,.02, ,
FLST,2,3,4
FITEM,2,6
FITEM,2,7
FITEM,2,1
AL,P51X
FLST,2,2,5,ORDE,2
FITEM,2,1
FITEM,2,3
AADD,P51X
ESIZE,0.0025,0,
MSHKEY,0
CM,_Y,AREA
ASEL, , , , 2
CM,_Y1,AREA
CHKMSH,'AREA'
CMSEL,S,_Y
!*
AMESH,_Y1
!*
CMDELE,_Y
CMDELE,_Y1
CMDELE,_Y2
!*
FLST,2,2,4,ORDE,2
FITEM,2,2
FITEM,2,10
!*
/GO
DL,P51X, ,ALL,
FLST,2,1,4,ORDE,1
FITEM,2,3
/GO
!*
SFL,P51X,PRES,.2e6,
FINISH
/SOL
/STATUS,SOLU
SOLVE
FINISH
/POST1
!*
PLESOL, S,EQV, 0,1.0

## Slide 7: Edited and Annotated Version
/PREP7 ! enter preprocessor
ET,1,PLANE82 ! specify plane82 as element type
KEYOPT,1,3,3 ! with thickness option
R,1,.003, ! real constant for 3mm thickness
MP,EX,1,200e9 ! define elastic modulus
MP,PRXY,1,0.3 ! define poisson's ratio
BLC4,0,0,.2,.02 ! make a 20cm by 2cm block with bottom left edge at origin
BLC4,.2,0,-.02,-.08 ! make a -2cm by -8cm block with bottom left edge at 20cm,0cm
AADD,1,2 ! add areas 1 and 2
LFILLT,9,8,.02, , ! make a .02 cm fillet between lines 9 and 8
AL,6,7,1 ! make an area from lines 6,7 and 2 (fillet region)
AADD,1,3 ! add areas 1 and 3
ESIZE,0.0025,0, ! set default element edge length to 2.5 mm
MSHKEY,0 ! specify free meshing
AMESH,all ! mesh all areas
LSEL,s,loc,x,0.2 ! select all lines with centroid at x=20 cm
DL,all, ,ALL, ! constrain these lines in all directions
LSEL,s,loc,y,0.02 ! select all lines with centroid at y=2 cm
SFL,all,PRES,.2e6, ! apply pressure on this line
allsel,all ! select everything
/SOL ! enter solution processor
SOLVE ! solve problem
/POST1 ! enter post processor
PLESOL, S,EQV, 0,1.0 ! plot equivalent stress

## Slide 8: Using Variables in Input Files
Plate with an offset hole
/PREP7 ! enter the preprocessor
len = 3 ! define full strip dimensions
wid = 1
rad = .1 ! define hole radius and center coordinates
xc = 0
yc = .25
ET,1,PLANE42 ! define element type as plane42
KEYOPT,1,3,3 ! specify constant thickness option
MP,EX,1,10e6 ! Elastic modulus
MP,PRXY,1,.3 ! Poisson's Ratio
R,.1 ! Set real constant for thickness
/PNUM,KP,1 ! Turn keypoint, line, and area numbering on
/PNUM,LINE,1
/PNUM,AREA,1
BLC4,0,-wid/2,len/2,wid ! Create Rectangle
CYL4,xc,yc,rad ! Create Circle
ASBA,1,2 ! Subtract area2 from area1
SMRTSIZE,1 ! Set smartsize control to 1
MSHKEY,0 ! free meshing
AMESH,all ! mesh all areas
lsel,s,loc,x,0 ! select all lines on symmetry plane
DL,all, ,symm, ! apply symmetry constraint
nsel,s,loc,x,0 ! select nodes at x=0
nsel,r,loc,y,-wid/2 ! select from selected set nodes at y=-wid
d,all,uy,0 ! fix selected node in uy to prevent rigid body motion
lsel,s,loc,x,len/2 ! select lines on free edge
SFL,all,PRES,-1000, ! apply pressure on lines
allsel,all ! select leverything
/SOL ! enter solution processor
SOLVE ! solve
/POST1 ! enter general postprocessor
PLNSOL, S,X, 0,1.0 ! plot x direction stresses
FINISH
len
wid