## Slide 1: Practice Problems for Axisymmetric Planar Elements
Jake Blanchard
Fall 2007

## Slide 2
E=100 GPa
=0.3
Axisymmetric
Fillet radius is 5 mm
P=1 MPa
Find max Von Mises stress
8 cm
4 cm
5 cm
6 cm

## Slide 3
Spinning disk, R=15 cm
E=71 GPa
=0.33
=2710 kg/m3
thickness=1 cm
Spin at 1000 rpm (must enter as radians/sec)
(Load is global rotation about y axis, under inertial loads)
Both stresses are 278 kPa at center
Hoop stress is 112 kPa at edge

## Slide 4
Spinning disk with reinforcement at axle
E=100 GPa
=0.3
=5000 kg/m3
Spin at 10 Hz
Fillets are 1 cm radius
Find max von mises stress
2 cm
1 cm
2 cm
12 cm
4 cm