## Slide 1: EMA 405
Coordinate Systems

## Slide 2: Introduction
There are many coordinate systems in ANSYS
Global and Local: used to locate geometry items (nodes, keypoints, etc.)
Display: determines systems in which geometry is displayed
Nodal: degree of freedom directions and nodal results
Element: material properties and element results
Results: transforms nodal or element results for listing or display (general postprocessor)
Working plane: used for drawing geometric primitives

## Slide 3: Results Coordinates
General Postprocessor/Options for Output
For cylindrical, x-direction is r-direction, y-direction is theta direction, z direction is axial direction

## Slide 4: Why do we need these
Element system: consider wood elements with grain at 45 degrees
Easiest to define E separately in grain direction and perpendicular direction (rotate element system 45 degrees)
x
y

## Slide 5: Why do we need these?
Orienting geometry elements
Rectangles are always oriented relative to working plane
To draw rectangle such as the one below, rotate the working plane

## Slide 6: Why do we need these?
Nodal coordinates
What if we have a set of forces oriented radially
Just select nodes on perimeter, change nodal coordinate system to cylindrical, and then set Fx

## Slide 7: Exercise
p
Only radial displacements
Only radial displacements
Inner radius=5 cm
Outer radius=10 cm
Angular extent = 45 degrees
E=200 GPa
=0.3
Pressure=1 MPa

## Slide 8: Exercise
p=1 MPa
E=200 GPa
=0.3
Inner radius is fixed
Inner radius = 5 cm
Outer radius = 10 cm