## Slide 1: EMA 405
3-D Elements

## Slide 2: Introduction
3-D elements have 3 degrees of freedom per node (ux, uy, uz)
The two fundamental shapes are hexahedral and tetrahedral elements

## Slide 3: Comments
Mesh generation is easier with tetrahedral elements
Tetrahedral elements tend to produce more degrees of freedom in a given model
Try mapped meshing if you want to use hex elements

## Slide 4: 4-node Tetrahedral element
Constant Strain

## Slide 5: 10-node Tetrahedral element
Linear Strain

## Slide 6: 8-node Hexahedral element
Linear Strain

## Slide 7: 20-node Hexahedral element
Quadratic Strain
Not compatible with 10-node tetrahedral elements

## Slide 8: Boundary Conditions
We have to restrict 3 translational rigid body modes and 3 rotational rigid body modes
We can restrict a single node in all 3 directions to take care of the translational modes
Rotations are trickier

## Slide 9: Boundary Conditions continued
Consider a 2-D case
With one node restricted in all directions, rotation about z-axis is possible
Restricting one node on x-axis in y-direction will prevent rotation about z
Do similar things to restrict rotations about x and y
x
y
Restrict in x and y
Restrict in y

## Slide 10: Example – hollow cylinder with hole
E=100 Gpa, =0.3
L=80 mm
Pressure load=1 Mpa (applied on end faces)
Inner radius=7.5 mm
Outer radius=10 mm
Radius of hole=2.5 mm
Theory says peak stress is 3.65 MPa