## Slide 1: Shell Elements
Jake Blanchard
Spring 2008

## Slide 2: Shell (or plate) Elements
These are typically “planar” elements
They are used to model thin structures which will experience bending
It is difficult to model thin structures with 3-D elements, because many are needed through thickness to capture bending behavior
Element features
  6 DOF per node (3 translations and 3 rotations) for 3-D elements
  Bending modes are included
  More than 1 stress at each point on the element

## Slide 3: Shell Elements in ANSYS
SHELL 61 = 2-node, axisymmetric shell – 4 DOF/node (3 translation and one rotation)
SHELL 208 = like 61, but finite strain
SHELL 209 = like 208, but with midside node (3-node element)
SHELL 28 = shear twist panel – 3 DOF/node (3 translation or 3 rotation)
SHELL 41 = 3-D quad or triangle with membrane only
SHELL 43 = 4-node shell with 6 DOF/node (plastic)
SHELL 63 = 4-node shell with 6 DOF/node (elastic only)
SHELL 93 = Like 63, but with midside nodes
SHELL 150 = 8-node p-element
SHELL 181 = 4-node, finite strain
SHELL 281 = 8-node, finite strain

## Slide 4: Real Constants
TK(I), TK(J), TK(K), TK(L)

## Slide 5: Assumed Behavior
Stresses are assumed to be linear through the thickness
Middle surface has 0 bending stress
Membrane stresses are uniform over thickness

## Slide 6: Boundary Conditions
Clamped Edge
  No displacements or rotations
Simply-Supported Edge
  No displacements
  Rotation is allowed perpendicular to edge

## Slide 7: Clamped Edges

## Slide 8: Simply Supported

## Slide 9: In-Class Problems
Consider a flat plate
1 m on each side
10 cm thick
E=200 GPa, =0.3
Uniform transverse pressure on entire face (1 MPa)
Two opposite sides are clamped, other two are simply supported
Expect max stress of 42 MPA, max displacement of 0.1 mm

## Slide 10: Circular plate
Plate is 1 m diameter (2R), 1 cm thick
Transverse pressure (1 MPa) is applied over inner circle with diameter of 20 cm (2r0)
E=200 Gpa, =0.3

## Slide 11: Pressure Vessel
End-Cap is hemispherical
R=2.2 m, t=0.2 m
P=1 MPa
E=200 Gpa, =0.3
R
2R