## Slide 1: Thermal Stresses
Jake Blanchard
Spring 2008

## Slide 2: Temp. Dependent Properties
For most materials, k is a function of temperature
This makes conduction equation nonlinear
ANSYS can handle this with little input from us
Examples:
  Copper: k=420.75-0.068493*T (W/m-K; T in K)
  Stainless Steel: k=9.01+0.015298*T
  Plot these vs. Temperature from 300 K to 1000 K
  Try:
  MP,KXX,1,420.75,-0.068493

## Slide 3: Incorporating into ANSYS
Input polynomial coefficients into Material Table
Set nonlinearity parameters
Everything else is the same

## Slide 4: In-Class Problems
Material 1 is Cu
Material 2 is SS
2
1
10 cm
1 cm
q=104 W/m2
h=1000 W/m2-K
Tb=50 C

## Slide 5: Thermal Stresses
Thermal stresses occur when there is differential expansion in a structure
  Two materials connected, uniform temperature change (different thermal expansion coefficients lead to differential expansion)
  Temperature gradient in single material (differential expansion is from temperature variation)

## Slide 6: Treating Thermal Stress in ANSYS
Two options
  Treat temperature distributions as inputs (useful for uniform temperature changes) – must input thermal expansion coefficient
  Let ANSYS calculate temperatures, then read them into an elastic/structural analysis

## Slide 7: Prescribing temperatures
Use: Preprocessor/Loads/Define Loads/Apply/Structural/Temperature/On Areas (for example)

## Slide 8: Sample
1=2*10-6 /K
E1=200 GPa
1=0.3
2=5*10-6 /K
E2=100 GPa
2=0.28
Increase T by 200 C
Inner radius=10 cm
Coating thickness=1 cm
2
1

## Slide 9: Calculating both temp and stress
Set jobname to ThermTest (File/Change Jobname…)
Main Menu/Preferences/Structural&Thermal&h-method
Input structural and thermal properties
Create geometry and mesh
Input thermal loads and BCs
Solve and save .db file
Delete all load data and switch element type to struct.
Edit element options if necessary
Apply BCs
Loads/Define Loads/Apply/Temperature/from thermal anal./ThermTest.rth
Solve

## Slide 10: Sample
1=2*10-6 /K
E1=200 Gpa
k1=10 W/m-K
1=0.3
2=5*10-6 /K
E2=100 Gpa
k2=20 W/m-K
2=0.28
Set outside T to 0 C
Set heating in 2 to 106 W/m3
Inner radius=10 cm
Coating thickness=1 cm
2
1

## Slide 11: In-Class Problems
Channels are 3 cm in diameter
k=20 W/m-K
E=200 Gpa
=0.3
= 10-5 /K
10 cm
q=104 W/m2
15 cm
2 cm
h=1000 W/m2-K
Tb=50 C