## Slide 1: Transient Thermal Problems
Jake Blanchard
Spring 2008

## Slide 2: Transient Analyses
So far, all the problems we’ve discussed in this class have all been steady state problems.
ANSYS is capable of doing a wide variety of transient problems.
We’ll explore this with a thermal problem.

## Slide 3: Sample Problem
Channel is 3 cm in diameter
k=80 W/m-K
=8000 kg/m3
cp=500 J/kg-K
Do steady state analysis now.
9 cm
q=104 W/m2
9 cm
3 cm
h=1000 W/m2-K
Tb=50 C

## Slide 4: Transient Problem
The question is, if we start the body at a uniform temperature of 50 C, how long does it take to reach steady state?

## Slide 5: Steps
Define time dependent loads (in load steps)
Set analysis parameters (time at end of load step, number of time steps, etc.)
Solve
Look at results

## Slide 6: Load History for Sample Problem
Load Step 1: Ramp up flux
Load Step 2: Flux is steady
Load Step 3: Turn off flux and let structure cool back to 50 C
1000
5000
q (W/m-K)
Time (s)
104

## Slide 7: Setting Up a Time Step
Set parameters for end of step (mostly loads)
Set time for end of step
Set number of time steps
Save settings

## Slide 8: First Load Step
Set analysis type to transient (Solution/Analysis Type/New Analysis)
Set time at end of step to 1,000 seconds (Solution/Analysis Type/Sol’n Controls)
Set initial temperatures (Define Loads/Apply/Initial Condition/Define)
Set convection and heat flux loads (heat flux is value at end of step)
Choose Ramped or Stepped
Only load is convection

## Slide 11: Post Processing
Options
  Read a load step, then do usual postprocessing (contour plots, etc.)
  Use time history processor to plot a particular value as a function of time
  Animate contours (try PlotCtrls/Style/Contours/Uniform Contours)

## Slide 12: Load Step 2
Only change is time at end of step (loads don’t change)
Solve

## Slide 13: Load Step 3
Delete heat flux
Set time at end (try 10,000 seconds)
Solve