## Slide 1: Uncertainty in Engineering - Introduction
Jake Blanchard
Fall 2010

## Slide 2: Instructor
Jake Blanchard
Engineering Physics
143 Engineering Research Building
blanchard@engr.wisc.edu

## Slide 3: Course Web Site
eCOW2

## Slide 4: Uncertainty Analysis for Engineers
Course Goals:
Students completing this course should be able to:
  create probability distribution functions for model inputs
  determine analytical solutions for output distribution functions when the inputs are uncertain
  determine numerical solutions for these same output distribution functions
  apply these techniques to practical engineering problems
  make engineering decisions based on these uncertainty analyses

## Slide 5: Grading
Homework – 30%
1 Midterm – 30%
Final Project – 40%
  Due Thursday, December 21, 2010

## Slide 6: Office Hours
Come see me any time
Email or call if you want to make sure I’m available

## Slide 7: Topics
Introduction to Engineering Uncertainty and Risk-Based Decision Making
Review of Probability and Statistics
Probability Distribution Functions and Cumulative Distribution Functions
Multiple Random Variables (joint and conditional probability)
Functions of Random Variables (analytical methods)
Numerical Models
  Monte Carlo
  Commercial Software
Statistical Inferences
Determining Distribution Models
  Goodness of Fit
  Software Solutions
Regression and Correlation
Sensitivity Analysis
Bayesian Approaches
Engineering Applications

## Slide 8: References
Uncertainty: A Guide to Dealing With Uncertainty in Quantitative Risk and Policy Analysis - Morgan & Henrion
Probability, Statistics, and Decision for Civil Engineers – Benjamin & Cornell
Risk Analysis: A Quantitative Guide – Vose
Probabilistic Techniques in Exposure Assessment – Cullen & Frey (on reserve)
Statistical Models in Engineering – Hahn & Shapiro (on reserve)
Probability Concepts in Engineering – Ang & Tang

## Slide 9: Uncertainty in Engineering
Engineers apply scientific and mathematical principles to design, manufacture, and operate structures, machines, processes, systems, etc.
This entire process brings with it uncertainty and risk
We must understand this uncertainty if we are to properly account for it

## Slide 10: Types of Uncertainty
Aleatory – uncertainty arising due to natural variation in a system
Epistemic – uncertainty due to lack of knowledge about the behavior of a system

## Slide 11: An Example
Aleatory – radioactive decay
  How long will it take for half of a sample to decay?
  When will a particular atom decay?
  Decay has an intrinsic uncertainty. No knowledge will help to reduce this uncertainty.
Epistemic – weather
  We’re never quite sure what tomorrow’s weather will be like, but our ability to predict has improved

## Slide 12: Some Examples

## Slide 13: Some Examples

## Slide 14: Some Examples

## Slide 15: Some Examples

## Slide 16: How Do We Deal With This?
Consider design of a diving board:

## Slide 17: Diving Board
We need to get stiffness right to achieve desired performance
We need to make sure board doesn’t fail
Options:
  Use worst-case properties and loads and small safety factor
  Use average properties and large safety factor
  Spend more on quality control for materials and manufacturing (still have uncertainty in loads)

## Slide 18: Sensitivity vs. Uncertainty
Consider the system pictured below:
x1
m
m
k
k
k
Fsin(t)

## Slide 19: Sensitivity
Suppose we have a design (k=2, m=1, =1) and we want to see how far we are from resonance
Resonant frequencies are 1 and 1.73 1
Or 1.41 and 2.45
Since the driving frequency is 1, we should be safe
To check, computing x 1 gives 0.6*F1

## Slide 20: Amplitude vs. Driving Freq. (F1=1)

## Slide 21: But What If Model Has Errors?
There are errors in the model:
  Inputs might be wrong
  Loads might be wrong
  Driving frequency might be wrong
  Etc.

## Slide 22: How Sensitive is the Result to Variations in Inputs?
Relative change in amplitude as a function of relative change in 3 inputs (k=2; m=1)

## Slide 23: Sensitivity for Different Defaults
k=10; m=1

## Slide 24: Defaults Closer to Resonance
k=1.1; m=1

## Slide 25: How Much Variation Do We Expect?
The final question is, how much variation do we expect in these inputs?
Can we control variation in spring stiffness and mass?
What about controlling the frequency?

## Slide 26: Uncertainty Analysis
Assume all inputs have normal distribution with standard deviation of 1% of the mean
Plot is histogram of amplitudes

## Slide 27: Uncertainty Analysis
What if inputs have standard deviation of 5% of the mean

## Slide 28: 10 Commandments of Analysis
Define the problem clearly
Let problem drive analysis (not available tools, for example)
Make the analysis as simple as possible
Identify all significant assumptions
Be explicit about decision criteria

## Slide 29: 10 Commandments (cont.)
Be explicit about uncertainties
  Technical, economic, and political quantities
  Functional form of models
  Disagreement among experts
Perform sensitivity and uncertainty analysis
  Which uncertainties are important
  Sensitivity=what is change in output for given change in input
  Uncertainty=what is best estimate of output uncertainty given quantified uncertainty in inputs

## Slide 30: 10 Commandments (cont.)
Iteratively refine problem statement and analysis
Document clearly and completely
Seek peer review